# Creating the ili9341_if

This is a collection of notes and observations during the creation of this module.

The need was for a display of some sort on an FPGA based controller. Most of the FPGA prototype boards have connectors for an Arduino shield; using a TFT sheild seemed like a good choice.

The desire was to use one with a parallel interface; supposedly this would be faster than one with a SPI interface.

## Hardware

The first attempt was to use the Vivado example AXI4-lite slave. The idea was to connect the TFT controller data instead of the internal registers.

The first discovery was that the ILI9341 is slow. Very slow. The minimum read pulse width is 45nS; the Vivado sample design allows one (1) clock for the read. The write time is better at 15nS, but that is still more than one CPU clock.

The timing diagram is in section 18.3 of the ILI9341 specification – page 238 (and page 240).

The second discovery was that the Vivado example design had two shortcomings:
1. It wasn’t possible to insert wait-states into that design.
2. It wasn’t designed for something that had a shared read/write bus.

I looked at a number of shared designs; I didn’t find one that used a shared bus, so I wrote a new one.

The first test was to send a READ_ID4 command and expect to read back 0x93, 0x41 from the controller. It always read back 0x00.

I had a simulation (in GHDL) running. I made an ILI9341 model that included timing checks. That all seemed to be OK.

I attached an ILA to the LCD signals to see what was happening. The timing looked good, but the data coming back was always 0x00.

I thought that it might be an issue with the chip; perhaps it was a clone and the ID4 register wasn’t implemented. I found some example initialization code and tried to configure the chip. The display started to respond.

I noticed in the code that special attention was given to the chip reset timing. I also saw in the data sheet that the minimum reset pulse width was 10uS (Section 15.4 – page 230). I created a software controlled reset line that starts with reset not asserted; now software was in total control.

Now I could get the display to do things (clear screen and draw line), but I still could not read the ID4 register. Looking at the example code there were no (0) reads from the controller.

After a number of web searches I found a comment that tri-state drivers were not inferred properly when the modules were synthesized out of context and that Global synthesis should be used for output products. Using global synthesis resulted with a warning message that the tri-state driver were not being inferred. This is a defect that I reported to Xilinx back in the Spartan-I days. You think they would have made some improvements in the last 20 years? Or are shared read/write buses (see comment about Vivado example design) something that they just do not understand?

OK, I instantiated the IOBUF’s directly. I set the read pulse width to very large and looked at the signals with the ILA. Turns out that the controller is even slower than documented. What I found to work is to that the minimum pulse width (45nS), divide by the AXI clock (10nS for 100 MHZ), round up to an integer, and add 1 to that. This seems to work – a rd pulse of 6 clocks at 100 MHz. I have not updated the model to reflect this finding.

The current hardware has the tri-state (IOBUF) debug lines exposed. I connect them to an ILA for testing; if they are unconnected the tool will rip up the logic.

## Interface Usage
There are 4 32-bit registers in the interface. Byte enables are ignored. Only bits [7:0] are sent to the controller.
0x0:	Command	Writing to this register sends a command to the controller. Command reads are not documented in the specification.
0x1:	Data	Read and write data from and to the controller.
0x2:	Reset	The reset line to the controller is on bit:0. It is high (reset removed) at power on.
0x3:	Multi Data	Self-timed writes of 2 or 4 bytes. U16->2 bytes, U32->4 bytes.

## Multi Data
The multi data register is to write multiple bytes to the controller. After the command is sent either 2 of 4 bytes can be sent with a single write. And additional generic was added to meet the write cycle time requirement of the controller.
## Simulation
A test-bench and GHDL Makefile are in the sim/ folder. It performs the one test listed above.

You need to have a unisim library built for your system. I used:
ghdl -a --workdir=unisim --work=unisim --ieee=synopsys $XILINX_VIVADO/data/vhdl/src/unisims/unisim_VCOMP.vhd
and
ghdl -a --workdir=unisim --ieee=synopsys $XILINX_VIVADO/data/vhdl/src/unisims/primitive/IOBUF.vhd
and
ghdl -a --workdir=work --ieee=synopsys $XILINX_VIVADO/data/vhdl/src/unisims/primitive/IOBUF.vhd
## Software

The most useful (to me) archive I found was at https://gist.github.com/postmodern/ed6e670999f456ad9f13.

The downloaded ZIP file contained source and header files that worked with little modification.

I have gotten parts of the ADAFruit GFX library ported over. Initial testing shows the screen updates to be much faster then they are with an Arduino; some of this may be from the faster processor, some of it may be from the streamlined interface.

If someone had the time and energy to port the entire library to uBlaze, that would be great.

## Future improvements

Most of the software doesn’t read from the controller, so improvements in the read time will have little benefit. Shaving clocks from the write time should help.

Look into the minimum TWRL pulse width. I currently use ceiling(TWRL/TAXI)+1 for writes. The +1 may not be needed.

Look at an early write acknowledge (axi_bvalid early). The processor can’t send writes back to back, so there is some time to finish the current write before another is received.

The reset line could be self timing. Writing a zero (to bit 0) would start a 10uS timer that would remove the reset. The software could poll this bit rather than use a timing loop. Perhaps writing a 1 to bit 0 to assert reset would be easier for the software to use? (23.08.23 – implemented) An advantage of a self-timed reset is that the 5us < TRW < 10us (AKA reset undefined) would be avoided. A disadvantage is that the counter would be large, and that would be a lot of gates for a ‘use once at power-up’ feature.

Added after this section was originally written: The Multi-Data register. The code typically sends three commands for a pixel: 1) Column select, 2) Page select, 3) Write memory. The select commands are followed by 4 byte writes, the write memory is followed by 2 byte writes. Turning these into self-timed multiple byte writes reduced the number of clocks for a pixel write to roughly 1/3 of the original number.

## PYNQ-Z2
Something I noticed bringing up the IP on this board is that the reset timing is sensitive. Sometimes it would work, most time it would not. Increasing the wait after the software reset seemed to have the greatest impact on how well it worked.

The processor in the MPSOC is a lot faster than a uBlaze. A lot. I don’t know what the AXI4 bus speed is, so I had to guess at the timing. A read delay of ‘7’ seem to be OK; my guess would be that it’s around 133~150 MHz. There is some tweaking and testing to do.

And find a Tcl script that sets paramaters based on the clock speed.